## Slide 1: Comparison of energy efficiency between macro and micro cells using energy saving schemes
Koustubh Sharma

## Slide 2: Lund University, Sweden
Education, research and innovation since 1666
Comparison of energy efficiency between macro and micro cells using energy saving schemes
Koustubh Sharma
Supervisors:
Zhi Zhang
Examiner:
Maria Kihl

## Slide 3: Introduction
ICT industry is responsible for 10% of world’s total energy consumption and is doubling in every 10 years. Cellular networks are among the main energy consumers in the ICT industry.
In Germany, last year mobile network operators spent more than 200 million Euros on electricity bills.
With IoT and connected cars, cellular networks are likely to densify furthermore.

## Slide 4: Problem Formulation
Need to study; comparison between macro centric and micro centric deployment.
The results presented in this thesis will contribute to the understanding of how these cells behave in a realistic traffic scenario and how much gain we can achieve by implementing the energy-saving schemes.

## Slide 5: Theory
MICROCELL
Microcells cover areas less than a kilometer in diameter and can often be seen mounted on signs, traffic lights, etc.
Macro and Micro cell
MACROCELL
Macrocells are traditional cell towers that cover from a few hundreds of meters to a few kilometers.

## Slide 6: Power distribution in base station
B
B
R
F
R
F
PA
P
A
feeder
P
out
P
in

## Slide 7: Power distribution in different cells
Chart: 
| PA | Main Supply | DC-DC | RF | BB | Cooling
Macro | 57 | 8 | 6 | 6 | 13 | 10
Chart: Micro
| PA | Main Supply | DC-DC | RF | BB
Macro | 38 | 8 | 7 | 9 | 38

## Slide 8: EARTH Power Model
P : Power consumed in the BS
P0 : Power consumed at no load
Pout : RF output power
Pmax: RF output power at maximum load
u: utilization
Δp: Slope of load dependent power consumption
BS type | NTRX | Pmax[W] | P0[W] | Δp | Psleep[W]
Macro | 2 | 40 | 130.0 | 4.7 | 75.0
Micro | 2 | 10 | 56.0 | 2.6 | 39.0

## Slide 9: EARTH Power Model
Fixed constant part
Power Consumed
utilization [%]
0
100
Load dependent part
BS type | NTRX | Pmax[W] | P0[W] | Δp | Psleep[W]
Macro | 2 | 40 | 130.0 | 4.7 | 75.0
Micro | 2 | 10 | 56.0 | 2.6 | 39.0

## Slide 10: Energy Saving schemes
Micro TX sleep
MBSFN
Lean carrier

## Slide 11: Micro TX Sleep
Radio Frame, 10ms
Notes: 5.6ms sleep time.

## Slide 12: MBSFN Sub-Frame
MBSFN Sub-Frames

## Slide 13: Lean Carrier

## Slide 14: Simulation Setup
Parameters | Value
Carrier frequency | 2.0 GHz
Bandwidth | 20 MHz
Modulation scheme | 64 QAM
Packet traffic model | Equal buffer model
Macro TX Power | 40 W per sector
Micro TX Power | 10 W
Macro cells in central grid | 21
Micro cells in central grid | 28
Feeder loss | 10 dB

## Slide 15: Macro Deployment

## Slide 16: Micro Deployment

## Slide 17: Results
  Comparison macro versus micro without energy saving schemes :
  Comparison of Power per area unit versus System throughput
Power per unit area difference at 100 Mbps/km2
31%

## Slide 18: Results
  Comparison of Energy per bit versus System throughput for central deployment of macro cells and micro cells.

## Slide 19: Results
  Comparison of bits per unit energy versus system throughput for central deployment of macro cells and micro cells.

## Slide 20: Results
  Comparison of DL user throughput for 50th and 95th percentile versus system throughput.

## Slide 21: Results
  Comparison macro with and without energy saving schemes
  Comparison of Power per area unit versus System throughput for central deployment of macro cells.
Scheme | Power per unit area difference at 100 Mbps/km2
Micro sleep | 6.89%
MBSFN | 9.92%
Lean | 16.89%

## Slide 22: Results
  Comparison of energy per bit unit versus system throughput for central deployment of macro cells.

## Slide 23: Results
  Comparison of bits per unit energy versus system throughput for central deployment of macro cells.

## Slide 24: Results
  Comparison micro with and without energy saving schemes
  Comparison of power per area unit versus system throughput for central deployment of micro cells.
Scheme | Power per unit area difference at 100 Mbps/km2
Micro sleep | 9.75%
MBSFN | 15.85%
Lean | 26.82%

## Slide 25: Results
  Comparison of energy per bit unit versus system throughput for central deployment of micro cells.

## Slide 26: Results
  Comparison of bits per unit energy versus system throughput for central deployment of micro cells.

## Slide 27: Results
  Comparison macro versus micro with energy saving schemes
  Comparison of Power per area unit versus System throughput for central deployment of macro cells versus micro cells.
Power per unit area difference at 100 Mbps/km2
50%

## Slide 28: Results
  Comparison of energy per bit unit versus system throughput for central deployment of micro cells versus macro cells.

## Slide 29: Results
  Comparison of bits per unit energy versus system throughput for central deployment of micro cells versus macro cells.

## Slide 30: Results
  Daily power consumption

## Slide 31: Comparative Chart
Deploy-ment | Scheme | Daily power consumption (kWhr/km2) | Yearly power consumption (kWhr/km2) | Difference at 10 Mbps edge cell DL user throughput
Macro | No scheme | 283.44 | 103,455.6 | 
 | Micro sleep | 263.52 | 96,184.8 | 7.02%
 | MBSFN | 254.64 | 92,943.6 | 10.16%
 | Lean | 234.62 | 85,637.7 | 17.22%
Micro | No scheme | 185.80 | 67,819.9 | 
 | Micro sleep | 161.23 | 58,849.6 | 13.22%
 | MBSFN | 150.24 | 54,837.6 | 19.13%
 | Lean | 125.85 | 45,937.4 | 32.26%

## Slide 32: Conclusions
31% of the energy could be saved by using micro cells instead of macro cells with no energy saving scheme.
The energy saving schemes saved up to 17% of energy in macros and 33% of energy in micros.
55% of the energy could be saved over a year by using micro cells with Lean Carrier instead of macro cells with no energy saving scheme.
Macros have better coverage than micro cells.

## Slide 33: Conclusions
Quite efficient to substitute macro cells with micro cells with energy saving schemes especially for densified 5G deployments.
Applying energy saving schemes in thousands of sites will save tens of millions of kilowatt hours (kWh) annually.

## Slide 34: Future Work
Energy efficiency could be studied in other scenarios as well such as sub-urban and rural.
There could be different sort of deployment of the cells to analyze the energy and throughput efficiencies.
One could make use of dynamic simulators to analyze the dynamic traffic.